PROCEDURES ON PLUGGING A WELL

2010  L.E.P.P.

Crawford County, Ks

Steps:

- Measure the water level with a weighted tape measure or string.

- Pour three (3) gallons of chlorine bleach into the well.

- Fill the well with sand and gravel to the water level which was measured instep one.  Use the weighted string or tape measure to determine when enough sand and gravel have been added.

- Fill the remaining open space with clay to a depth of six (6) feet below ground surface.

- Use an approved cement or bentonite grout to fill the well from six (6) feet to three (3) feet below ground surface.

- Cut the well casing off three (3) feet below ground surface and back fill with surface soils.

Option 2:

Simply fill the wall from bottom depth to three (30 feet below ground surface with an approved cement or sodium bentonite grout then backfill the well with surface soils from three (3) feet to round surface.

ANY QUESTIONS, CONTACT BILL TOWERY AT THE CRAWFORD COUNTY ENVIRONMENTAL HEALTH DEPARTMENT AT 620-724-7088 OR THE ZONING OFFICE AT 620-724-6168.

Thank you.