REMOVAL OR FILLING OF ABANDONED SEPTIC TANKS

PROCEDURE FOR FILLING SEPTIC TANKS

STEP I.	Remove the Liquids and Sludge:

Pump any water, semi-sold or solid organic materials from the septic tank.  This material should be disposed of at a permitted wastewater treatment facility.  Pumping should be done by a licensed septage hauler.

STEP II.	Puncture the Floor:

It is important that water not accumulate inside the old tank.  The floor should have holes drilled in it or the floor can be broken up in place to prevent the accumulation of water.

STEP III.	Plugging and Filling the Septic Tank:

The septic tank should be plugged or filled with low-organic soil or clay material.  Be sure this material contains no other potential contaminants and is moist enough to compact easily.  The fill material may be sand, grave, concrete, clay, dirt, or other approved by the County Health Department.

STEP IV	Removal of Septic Tank:

In some cases the septic tank may be removed and disposed of at a permitted landfill.  The remaining hole should then be filled with dirt or clay.